## Slide 1: CS 367-305/306/307
Recitation 10 – Y86-64/Logic Gates

## Slide 2: Y86-64
Say we have the following encoding
What’s the first instruction?
What about the next one?
60 | 76 | 90 | 00 | 00 | 00 | 00 | 00

## Slide 3: Y86-64
Say we have the following encoding
What’s the first instruction?
  addq
What about the next one?
60 | 76 | 90 | 00 | 00 | 00 | 00 | 00

## Slide 4: Y86-64
Say we have the following encoding
What’s the first instruction?
  addq %rdi, %rsi;
What about the next one?
60 | 76 | 90 | 00 | 00 | 00 | 00 | 00

## Slide 5: Y86-64
Say we have the following encoding
What’s the first instruction?
  addq %rdi, %rsi;
What about the next one?
  retq;
60 | 76 | 90 | 00 | 00 | 00 | 00 | 00

## Slide 6: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
0x400000

## Slide 7: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
rrmovq %rdi, %rcx subq %rax, %rcx
0x400000

## Slide 8: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
rrmovq %rdi, %rcx subq %rax, %rcx
jl L2
0x400000

## Slide 9: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
rrmovq %rdi, %rcx subq %rax, %rcx
jl L2
0x400000 20 71

## Slide 10: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
rrmovq %rdi, %rcx subq %rax, %rcx
jl L2
0x400000 20 71
0x400002 61 01

## Slide 11: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
rrmovq %rdi, %rcx subq %rax, %rcx
jl L2
0x400000 20 71
0x400002 61 01
0x400004 72 10 00 40 00 00 00 00 00 #if L2 starts at 0x400010, for example

## Slide 12: Y86-64
cmpq %rax, %rdi
jl L2
X86-64
Y86-64 equivalent
Memory Encoding
rrmovq %rdi, %rcx subq %rax, %rcx
jl L2
0x400000 20 71
0x400002 61 01
0x400004 72 10 00 40 00 00 00 00 00 #if L2 starts at 0x400010, for example
0x40000d … #jl took 9 bytes, so the next starting address is 0x400004 + 9

## Slide 13: Logic Gates

## Slide 14: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | 
Decode | 
Execute | 
Memory | 
Write Back | 
PC Update | 
61 | 67
M[0x110]
M[0x111]

## Slide 15: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | icode:ifun <- 6:1 rA:rB <- 6:7 valP <- 0x112
Decode | 
Execute | 
Memory | 
Write Back | 
PC Update | 
61 | 67
M[0x110]
M[0x111]

## Slide 16: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | icode:ifun <- 6:1 rA:rB <- 6:7 valP <- 0x112
Decode | valA <- R[%rsi] = 8 valB <- R[%rdi] = 16
Execute | 
Memory | 
Write Back | 
PC Update | 
61 | 67
M[0x110]
M[0x111]

## Slide 17: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | icode:ifun <- 6:1 rA:rB <- 6:7 valP <- 0x112
Decode | valA <- 8 valB <- 16
Execute | valE <- 16 – 8 = 8 ZF=0, SF=0, OF=0
Memory | 
Write Back | 
PC Update | 
61 | 67
M[0x110]
M[0x111]

## Slide 18: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | icode:ifun <- 6:1 rA:rB <- 6:7 valP <- 0x112
Decode | valA <- 8 valB <- 16
Execute | valE <- 8 ZF=0, SF=0, OF=0
Memory | 
Write Back | R[%rdi] <- 8
PC Update | 
61 | 67
M[0x110]
M[0x111]

## Slide 19: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | icode:ifun <- 6:1 rA:rB <- 6:7 valP <- 0x112
Decode | valA <- 8 valB <- 16
Execute | valE <- 8 ZF=0, SF=0, OF=0
Memory | 
Write Back | R[%rdi] <- 8
PC Update | PC <- 0x112
61 | 67
M[0x110]
M[0x111]

## Slide 20: Y86-64 CPU Stages
Stage | subq %rsi, %rdi
Fetch | icode:ifun <- 6:1 rA:rB <- 6:7 valP <- 0x112
Decode | valA <- 8 valB <- 16
Execute | valE <- 8 ZF=0, SF=0, OF=0
Memory | 
Write Back | R[%rdi] <- 8
PC Update | PC <- 0x112
61 | 67
M[0x110]
M[0x111]